## Slide 1: Design and integration of project-specific ontology for data analytics support
Miloš Šipetić, Reinhard Jentsch, Judit Aizpuru, Jan Kurzidim
Austrian institute of technology
Linked data in architecture and construction 2020

## Slide 2: Inbetween project
H2020 project
Grant Agreement number: 768776
https://www.inbetween-project.eu/
2018-2020
Co-funded by the Horizon 2020 programme of the European Union

## Slide 3: System architecture

## Slide 4: Motivation for the ontology
Different demonstration sites
Different technologies used
Different kinds of third-party data (sources external to the project)
Time series metadata
Development of (semi-)automated commissioning procedure
Development of generalized analytics pipelines
Usage of collected data by multiple stakeholders

## Slide 5: Data needs
List of all the intended energy actions and analyses
Lists of:
  time series
  Metadata
  Other data
E.g. Detecting energy waste (any kind of heating device turned on while temperature within normal bounds)
    Temperature measurements from rooms
    Heating bodies consumption or on/off information per room
    Size of apartment
    Usual number of occupants…

## Slide 6: Identified important concepts
Sensors
Actuators
Meters
Spaces
Site/dwelling description + topology
Monitoring time series description
Third party data (weather data, weather forecasts)
ML results (prediction models+descriptions)

## Slide 7: Ontologies to reuse
Analysis of existing ontologies
Identification of most promising for reuse based on
  Domain coverage
  Level of (community) support
  Research interest
BOT
SAREF
SAREF4BLDG

## Slide 8: Imports graph
BOT
SAREF
SAREF4BLDG
INBETWEEN
* SAREF4BLDG
Alignment module
TIME
* SAREF
Alignment module
* G.F. Schneider - Towards aligning domain ontologies with the building topology ontology

## Slide 9: Time series related classes

## Slide 10: Building elements specializations

## Slide 11: Space usage

## Slide 12: Additional data and object properties

## Slide 13: Data collection and integration
Demonstration site survey
Transformation into triplets
Usage
Third-party data
Occupant questionnaires
Device ids
Setup of transformation rules
Site plans
Description of data points
Linking to time series storage
Commissioning data collection
Locations
Links to monitoring data storage
Transformation into table format
Transformation of the collected dataset

## Slide 14: Cellfie

## Slide 15: Use cases

## Slide 16: Virtual occupancy sensor – Motivation
Direct occupancy detection methods are
  Expensive
  Privacy invading
  imprecise
Usually based on
  Cameras
  Person counting
  Motion sensors with time threshold
For specific residential scenarios useful to have occupancy information
With additional information it is possible to use motion sensors to infer occupancy

## Slide 17: Virtual occupancy sensor – solution
Interpret contextual data to infer occupancy
  Dwelling entrance door status
  Motion sensor data
Need to know:
  topology in very rough outlines
  Time series references

## Slide 18: Virtual occupancy sensor – state change diagram
Door opened
Door closed
Timeout
Motion
Timeout
Timeout
Timeout
Timeout
Motion
Motion
Motion
Motion
Door opened
Door
opened
Door opened
Door closed
No
occupancy
Occupancy
Open
Closed
(transition)

## Slide 19: Virtual occupancy sensor - queries
SELECT ?apartment ?timeseries_ref WHERE {
?apartment a inbetween:Apartment.
?apartment bot:containsZone ?space.
?space bot:adjacentElement ?wall.
?wall a inbetween:InternalWall.
?wall inbetween:hostsElement ?door.
?door inbetween:hostsElement ?sensor.
?sensor bot:hasSubElement ?doorsens.
?doorsens a inbetween:DoorWindowSensor.
?doorsens inbetween:hasTimeSeries ?timeseries_ref
}
:Apartment
bot:containsZone
bot:Space
bot:adjacentElement
:hostsElement
:InternalWall
:EntranceDoor
:hostsElement
:DoorWindowSensor
:DoorSensor
bot:hasSubelement
:hasTimeSeries
:InfluxDbTimeSeries

## Slide 20: Virtual occupancy sensor - queries
SELECT ?apartment ?sensor ?timeseries_ref WHERE {
?apartment a inbetween:Apartment.
?apartment bot:containsElement ?sensor.
?sensor bot:hasSubElement ?motionsensor.
?motionsensor a inbetween:MotionSensor.
?motionsensor inbetween:hasTimeSeries ?timeseries_ref
}

## Slide 21: Virtual occupancy sensor - results

## Slide 22: Cluster analysis of electricity consumption
Difficult to interpret multiple multi-day, week or month continuous time series
Grouping on intervals and similarity facilitates understanding
Clustering methods (K-Means, Agglomerative, Gaussian mixture…)
Where possible consumptions are grouped according to type
  Heating, hot water, rest
Information from the knowledge base used to compile lists

## Slide 23: Cluster analysis – heating consumption query
SELECT ?apartment ?timeseries_ref WHERE {
?apartment a inbetween:Apartment.
?apartment bot:containsElement ?radiator.
?smartplug inbetween:controlsElement ?radiator.
?smartplug bot:hasSubElement ?sensor.
?sensor a inbetween:PowerSensor.
?sensor inbetween:hasTimeSeries ?timeseries_ref
}

## Slide 24: Cluster analysis – total consumptions query
SELECT ?apartment ?sensor ?subsensor ?timeseries_ref WHERE {
?apartment a inbetween:Apartment.
?sensor inbetween:metersZone ?apartment.
?sensor bot:hasSubElement ?subsensor.
?subsensor a inbetween:PowerSensor.
?subsensor inbetween:hasTimeSeries ?timeseries_ref
}

## Slide 25: Cluster analysis ontology concerns

## Slide 26: Conclusions
Resulting knowledge base was successfully used to solve problems within the project
Performance
Demonstration site changes tracking needs to be solved
  Knowledge base concerns
  Time series database concerns
Publishing the ontology

## Slide 27: Thank you for your attention
Contact:
Milos.Sipetic@ait.ac.at