## Slide 1
Real-Time Building Performance Monitoring using Semantic Digital Twins
Alex Donkers – PhD Candidate at Eindhoven University of Technology – a.j.a.donkers@tue.nl
Dujuan Yang, Bauke de Vries, Nico Baken

## Slide 2
BSC ARCHITECTURE, URBANISM & BUILDING SCIENCES TU/e
MSC CONSTRUCTION MANAGEMENT & ENGINEERING TU/e
PHD CANDIDATE TU/e x KPN
Bauke de Vries, Nico Baken & Dujuan Yang
linktr.ee/AlexDonkers
in/AlexDonkers
@Alex_Donkers

## Slide 3
Virtual representation
Indoor environment
Update (information)
(Update
(data)
Notes: The talk today focusses on the indoor climate and how the building could improve this climate.
Growing importance
IEQ influences user satisfaction
IEQ influences workplace satisfaction
Influences productivity
Influences student learning performance
Bad IEQ results in health issues, e.g. asthma and increasing short-absence of knowledge workers and Sick Building Syndrome symptoms.

## Slide 4
Indoor Environmental Quality
Thermal comfort
Acoustic comfort
Visual comfort
Air quality
Natural ventilation
CO2 level
Particulate matter
Mechanical ventilation
Reverberation time
Background noise level
Communication privacy
Mean radiant temperature
Relative humidity
Surface temperature
Air velocity
Geometry of rooms and elements
Building topology
Weather information
Occupant preferences
Activity level
Glare
Natural light
Artificial light
Visual privacy
Sociodemographics
Mood
Clothing level
Metabolic rate

## Slide 5: Mean radiant temperature
Ts,2
Ts,3
Ts,1
Ts,4
Ts,5
As,2 *
Thermal transmittance
Indoor air temperature
Indoor air velocity
Indoor heat transfer coefficient
Outdoor air temperature
Outdoor air velocity
Outdoor relative humidity
Sun intensity
Sun azimuth
Height of the sun
Surface tilt
Surface azimuth
Notes: To show the complexity of monitoring IEQ:

## Slide 6
TOPOLOGY
Rooms
Elements
How they relate to each other
STATIC PROPERTIES
Geometry
Material characteristics
DYNAMIC PROPERTIES
Sensor data
Weather data
Challenge
Integrate the heterogeneous information related to indoor environmental quality assessments.
Notes: To generalize this, we typically distinguish three data categories.
…
To perform the previous calculation, we would need a homogeneous representation of data.

## Slide 7: Building Topology Ontology (BOT)

## Slide 8: Approaches to describe property values
GRAPH DATABASE
GRAPH DATABASE
TIME-SERIES DATABASE
S01,21,1630575705
S01,21,1630575706
S01,22,1630575709
:Building
:Room
:Sensor01
:Temperature
:Observation01
“21”
“1630575705”
“21”
“1630575706”
:Observation02
:value
:value
:time
:time
:hasSpace
:hasSensor
:observes
:hasResult
:hasResult
:Building
:Room
:Sensor01
:Temperature
:hasSpace
:hasSensor
:observes
:timeSeriesReference
“InfluxDB-S01”
READ MORE
Tang et al. (2019)
Notes: First approach is good for static properties
Second is better for

## Slide 10: Static and dynamic properties
ONTOLOGIES FOR DYNAMIC PROPERTIES
Semantic Sensor Network Ontology (SSN)
Sensor, Observation, Sample and Actuator (SOSA)
Smart Applications REFerence Ontology (SAREF)
Brick
ONTOLOGIES FOR STATIC PROPERTIES
Ontology for Property Management (OPM)
BIM Design Ontology (BIMDO)
Building Product Ontology (BPO)
:Property
Value
:PropertyState
:FeatureOfInterest
:Sensor
:Property
:FeatureOfInterest
:Observation
Value
:Result

## Slide 11: Building Performance Ontology
BOP
https://w3id.org/bop
Based on design patterns and best practices of 70 ontologies
Homogeneously describing static and dynamic property values
Implements 4 levels of detail
Versioning of properties
Property sets
Generic upper ontology & use-case specific lower-level ontologies

## Slide 12: Building Performance Ontology
Executor
Property
FeatureOfInterest
Execution
Result
hasFeatureOfInterest/
isFeatureOfInterestOf
executedBy/
performsExecution
hasExecutedProperty /
hasExecution
hasProperty min 1/
isPropertyOf min 1
executesOn/
isExecutedBy
Value
hasValue max 1
Unit
hasSimpleUnit max 1
Unit
hasUnit max 1/
isUnitOf
Database
hasExternalDatabase/
isDatabaseOf
hasSubProperty/
isSubPropertyOf
PropertySet
containsProperty /
ispartOfPropertySet
TimeOfGeneration
prov:generatedAtTime
^^xsd:dateTime
DataPoint
Procedure
usesProcedure/
isUsedFor
implementsProcedure/
implementedBy
hasSubExecutor/
isSubExecutorOf
Platform
hosts min 1/
isHostedBy max 1
hasDataPoint/
isDataPointOf
hasComplexProperty/
isComplexPropertyOf
hasResult/
isResultOf
hasPropertyState/
isPropertyStateOf
hasSimpleResult max 1
hasSimpleProperty
hasSimplePropertyState
rdfs:subClassOf
owl:ObjectProperty
owl:DatatypeProperty
rdfs:Class
rdfs:Literal
Input
Output
UserDefined
ID
hasID max 1
Class
Literal
UPPER ONTOLOGY

## Slide 13: Building Performance Ontology
Sensor
Property
FeatureOfInterest
Observation
Result
hasFeatureOfInterest/
isFeatureOfInterestOf
observedBy/
performsObservation
hasObservedProperty /
hasObservation
hasProperty min 1/
isPropertyOf min 1
observes/
isObservedBy
Value
hasValue max 1
Unit
hasSimpleUnit max 1
Unit
hasUnit max 1/
isUnitOf
Database
hasExternalDatabase/
isDatabaseOf
hasSubProperty/
isSubPropertyOf
PropertySet
containsProperty /
ispartOfPropertySet
TimeOfGeneration
prov:generatedAtTime
^^xsd:dateTime
DataPoint
Procedure
usesProcedure/
isUsedFor
implementsProcedure/
implementedBy
hasSubSensor/
isSubSensorOf
Platform
hosts min 1/
isHostedBy max 1
hasDataPoint/
isDataPointOf
hasComplexProperty/
isComplexPropertyOf
hasResult/
isResultOf
hasPropertyState/
isPropertyStateOf
hasSimpleResult max 1
hasSimpleProperty
hasSimplePropertyState
rdfs:subClassOf
owl:ObjectProperty
owl:DatatypeProperty
rdfs:Class
rdfs:Literal
Input
Output
UserDefined
ID
hasID max 1
Class
Literal
SENSOR PATTERN

## Slide 14: Building Performance Ontology
Actuator
Property
FeatureOfInterest
Actuation
Result
hasFeatureOfInterest/
isFeatureOfInterestOf
actuatedBy/
performsActuation
hasActuatedProperty /
hasActuation
hasProperty min 1/
isPropertyOf min 1
actsOn/
isActuatedBy
Value
hasValue max 1
Unit
hasSimpleUnit max 1
Unit
hasUnit max 1/
isUnitOf
Database
hasExternalDatabase/
isDatabaseOf
hasSubProperty/
isSubPropertyOf
PropertySet
containsProperty /
ispartOfPropertySet
TimeOfGeneration
prov:generatedAtTime
^^xsd:dateTime
DataPoint
Procedure
usesProcedure/
isUsedFor
implementsProcedure/
implementedBy
hasSubActuator/
isSubActuatorOf
Platform
hosts min 1/
isHostedBy max 1
hasDataPoint/
isDataPointOf
hasComplexProperty/
isComplexPropertyOf
hasResult/
isResultOf
hasPropertyState/
isPropertyStateOf
hasSimpleResult max 1
hasSimpleProperty
hasSimplePropertyState
rdfs:subClassOf
owl:ObjectProperty
owl:DatatypeProperty
rdfs:Class
rdfs:Literal
Input
Output
UserDefined
ID
hasID max 1
Class
Literal
ACTUATOR PATTERN

## Slide 15: Building Performance Ontology
Executor
Property
FeatureOfInterest
Execution
Result
hasFeatureOfInterest/
isFeatureOfInterestOf
executedBy/
performsExecution
hasExecutedProperty /
hasExecution
hasProperty min 1/
isPropertyOf min 1
executesOn/
isExecutedBy
Value
hasValue max 1
Unit
hasSimpleUnit max 1
Unit
hasUnit max 1/
isUnitOf
Database
hasExternalDatabase/
isDatabaseOf
hasSubProperty/
isSubPropertyOf
PropertySet
containsProperty /
ispartOfPropertySet
TimeOfGeneration
prov:generatedAtTime
^^xsd:dateTime
DataPoint
Procedure
usesProcedure/
isUsedFor
implementsProcedure/
implementedBy
hasSubExecutor/
isSubExecutorOf
Platform
hosts min 1/
isHostedBy max 1
hasDataPoint/
isDataPointOf
hasComplexProperty/
isComplexPropertyOf
hasResult/
isResultOf
hasPropertyState/
isPropertyStateOf
hasSimpleResult max 1
hasSimpleProperty
hasSimplePropertyState
rdfs:subClassOf
owl:ObjectProperty
owl:DatatypeProperty
rdfs:Class
rdfs:Literal
Input
Output
UserDefined
ID
hasID max 1
Class
Literal
STATIC PROPERTY PATTERN

## Slide 16
Open Smart Home
                Apartment in Germany
                Original dataset by Schneider and Rasmussen http://doi.org/10.5281/zenodo.1244602
                Sensor data: temperature, brightness, relative humidity
                .ttl in BOP-vocabulary
TAKE ME THERE
github.com/AlexDonkers/OpenSmartHome

## Slide 17
RULES AND REGULATION
PMV
PPD
PYTHON
Real-time thermal comfort monitoring
STATIC PROPERTIES
Geometry
Material characteristics
DYNAMIC PROPERTIES
Sensor data
Weather data
TOPOLOGY
Rooms
Elements
Convert to linked data
12:00 21
12:10 21
12:20 22
12:40 21
:OSH_TSDB
ofo:Database
bop:isDataPointOf
Link to external DB
:Wall_02
bop:FeatureOfInterest
:Room_01
bop:FeatureOfInterest
bot:adjacentElement
:TemperatureSensor_01
bop:Sensor
:Wall_01
bop:Platform
bop:hosts
bot:adjacentElement
:M
bop:Unit
:Wall_02_Length
bop:Property
_:bn
bop:Result
bop:hasProperty
“12.0”
bop:hasPropertyState
bop:hasUnit
bop:hasValue
:Room_01_Temperature
bop:Property
:R01_T_Point
bop:DataPoint
bop:hasPropertyState
:DEG_C
bop:Unit, unit:DEG_C
bop:hasUnit
“OSH_T_0001”
bop:hasID

## Slide 18: Workflow
Python
pythermalcomfort
Python script
GraphDB
Revit
RVT
IFC
RDF Turtle
IFC-to-LBD converter
RDF Turtle
Open Smart Home
Sensor Data
CSV
InfluxQL INSERT commands
InfluxDB
Sensor data
Query linked building data
ASHRAE-55
PDF
RDF
GraphDB
RDF
Query time-series data
Query regulations
Thermal Comfort
manual conversion
manual conversion
manual conversion
SPARQLwrapper library
influxdb library
SPARQLwrapper library
inspired by
Notes: This workflow could be generalized for many use-cases in the operational phase of buildings.

## Slide 19: Open Smart Home

## Slide 20: TEMPERATURE GraphDB
graph_url = "http://localhost:7200/repositories/OpenSmartHomeRepository"
sparql = SPARQLWrapper(graph_url)
sparql.setQuery("""PREFIX props: <https://w3id.org/props#>
PREFIX quantitykind: <http://qudt.org/vocab/quantitykind/>
PREFIX bot: <https://w3id.org/bot#>
PREFIX bop: <https://w3id.org/bop#>
PREFIX : <https://research.tue.nl/nl/persons/alex-ja-donkers#>
SELECT ?property ?datapoint ?database
WHERE {
?room bop:hasSimplePropertyState "Bedroom" ;
bot:containsElement ?sensor .
?sensor bop:observes ?property .
?property a quantitykind:Temperature ;
bop:hasPropertyState ?datapoint .
?datapoint bop:isDataPointOf ?database .
} """)

## Slide 21: TEMPERATURE InfluxDB
client = InfluxDBClient(host='localhost', port=8086)
client.switch_database(database)
resultset = client.query(
'SELECT ‘ + property + ’ FROM ’ + datapoint + ‘ WHERE time <= ‘ + str(maxTime) + ‘ AND time > ‘ + str(minTime) + ‘ ORDER BY time DESC LIMIT 1’)
value = list((resultset.get_points(measurement=datapoint)))
temperature = value[0]['value']
Notes: Here, I selected a minTime and maxTime. But we can also query the most recent value and make a continuous loop in Python with a certain frequency (e.g. every 10 minutes).

## Slide 22: GEOMETRY GraphDB
sparql.setQuery("""PREFIX props: <https://w3id.org/props#>
PREFIX quantitykind: <http://qudt.org/vocab/quantitykind/>
PREFIX bot: <https://w3id.org/bot#>
PREFIX bop: <https://w3id.org/bop#>
PREFIX beo: <http://pi.pauwel.be/voc/buildingelement#>
PREFIX : <https://research.tue.nl/nl/persons/alex-ja-donkers#>
SELECT ?room ?wall ?interface ?interfaceWidthValue
WHERE {
?room bop:hasSimplePropertyState "Bedroom" ;
bot:adjacentElement ?wall .
?wall a beo:Wall .
?interface bot:interfaceOf ?room, ?wall ;
bop:hasProperty ?width .
?width a quantitykind:Width ;
bop:hasPropertyState / bop:hasValue ?interfaceWidthValue
} """)

## Slide 23: Results: PMV and PPD

## Slide 24: Results: PMV and PPD improvements

## Slide 25
Conclusions
IEQ affects occupants' satisfaction, health and productivity
IEQ assessments use heterogeneous data
BOP enables the integration of topological building information with static and dynamic property values
A python script used the integrated data to perform real-time thermal comfort assessments using the Open Smart Home
Based on the available data, significant improvements of the IEQ performance are possible

## Slide 26
17:30:22
Your feedback has been processed
CO2
v
v
Next up

## Slide 27
Future research directions
Occupant data
Pattern recognition
System control
Conversion tools
Ontology alignment

## Slide 28: Online documentation
TAKE ME THERE
w3id.org/bop

## Slide 29: Online documentation
TAKE ME THERE
w3id.org/bop
UPPER ONTOLOGY
USE-CASE SPECIFIC ONTOLOGIES
Sensor pattern
Actuator pattern
Static properties pattern
EXAMPLES
Using BOP in practice
Use-case specific example graphs
Example queries
ALIGNMENTS TO OTHER ONTOLOGIES
BOP x OPEN DIGITAL TWINS
OPEN SMART HOME
Various file formats (.rvt, .ttl, .dae, .gltf)
Sensor data
CSV-to-InfluxDB converter
TWO UPCOMING PROJECTS
Open Flat Open Family Home

## Slide 30
Alex Donkers – PhD Candidate at Eindhoven University of Technology – a.j.a.donkers@tue.nl
Dujuan Yang, Bauke de Vries, Nico Baken
Notes: This paper contributes to the long-term goal of improving IEQ in buildings and reducing the gap between measured and perceived IEQ.
Ultimately, we should improve the quality of life in our buildings